Puruimuri – Dust collector
Turvallisuus / Vältä metallin ja isojen kappaleiden joutumista puruimuriin / Käyttö / Avaa tarvittavat sulkupellit - Open the needed blast gates / Käynnistä puruimuri ohjauspainikkeesta / Jos imuri ei käynnisty napista katso kohta ”Viikkotarkistus” / Käytön jälkeen sulje sulkupellit ja sammuta imuri / Viikkotarkistus / Imuri on tarkastettava joka tiistai sekä hätäseis-nappejen käytön jälkeen. / Mene pylväsporakoneen viereisestä ovesta imurin luo / Tarkista että purusäkit ovat ehjiä ja etteivät ne ole täynnä / Heiluta kankaisia suodatinsäkkejä, jotta niihin tarttunut puru irtoaa / Kuittaa imuri käyttövalmiiksi ulko-oven viereisestä vihreästä painikkeesta	Safety / Avoid vacuuming metal and big pieces / Usage / Open the needed blast gates / Start the dust collector with the remote control buttons / If the dust collector doesn’t start refer to the weekly inspection section / After use close the blast gates and turn the dust collector off / Weekly inspection / The dust collector needs to be inspected weekly or after using the room wide emergency stops. / Go up the stars from the exit door near the drill press / Inspect the dust bags for holes and verify they aren’t full / Shake the cloth filter bags to release accumulated dust / Re-enable the dust collector from the green button next to the door